Memory management
Memory management functions in C library will allow us to allocate, alter allocated memory and deallocate allocated memory as when required

---
Memory management Functions
Syntax
#include <stdlib.h>
void * malloc( unsigned int size );
The malloc function allocates space for an object whose size is specified by size and returns pointer to (lowest byte address) newly allocated memory of type void.
There is no guarantee that malloc will allocate memory every time we call. If malloc fails to allocate memory because of any reason it returns NULL as return value.
The lifetime of an allocated object extends from the allocation until the deallocation.

---
Deallocating memory allocated
void free(void *ptr);
The free function causes the space allocated by malloc pointed to by ptr to be deallocated, that is, made available for further allocation.

---
Allocating memory for array of objects
void *calloc(size_t nmemb, size_t size);
The calloc function allocates space for an array of "nmemb objects", each of whose size is "size". The space is initialized to all bits zero and returns pointer to (lowest byte address) newly allocated memory of type void.
Returns NULL id failed to allocate new memory.

---
Alter the memory allocated by malloc or calloc
void *realloc(void *ptr, size_t size);
The realloc function deallocates the old object pointed to by ptr and returns a pointer to a new object that has the size specified by size.
The contents of the new object shall be the same as that of the old object prior to deallocation.

---
Alter the memory allocated by malloc or calloc
If "ptr" is a null pointer, the realloc function behaves like the malloc function for the specified size.
If ptr does not match a pointer earlier returned by the calloc, malloc, or realloc function, or if the space has been deallocated, the behavior is undefined.
If memory for the new object cannot be allocated, the old object is not deallocated and its value is unchanged.
The realloc function returns a pointer to the new object (which may have the same value as a pointer to the old object), or a null pointer if the new object could not be allocated.