Committee Draft — ISO/IEC 9899:TC2
Types
Types are partitioned into object types (types that fully describe objects), function types (types that describe functions), and incomplete types (types that describe objects but lack information needed to determine their sizes).
An object declared as type _Bool is large enough to store the values 0 and 1.
An object declared as type char is large enough to store any member of the basic execution character set. If a member of the basic execution character set is stored in a char object, its value is guaranteed to be nonnegative.
An object declared as type signed char occupies the same amount of storage as a ‘‘plain’’ char object. A ‘‘plain’’ int object has the natural size suggested by the architecture of the execution environment (large enough to contain any value in the range INT_MIN to INT_MAX as defined in the header <limits.h>).
For each of the signed integer types, there is a corresponding (but different) unsigned integer type (designated with the keyword unsigned) that uses the same amount of storage (including sign information)
There are three real floating types, designated as float, double, and long double.32) The set of values of the type float is a subset of the set of values of the type double; the set of values of the type double is a subset of the set of values of the type long double
The type char, the signed and unsigned integer types, and the floating types are collectively called the basic types.
The three types char, signed char, and unsigned char are collectively called the character types. The implementation shall define char to have the same range, representation, and behavior as either signed char or unsigned char.

---
Types
Integer and floating types are collectively called arithmetic types.
The void type comprises an empty set of values; it is an incomplete type that cannot be completed.
Any number of derived types can be constructed from the object, function, and incomplete types, as follows:
Array type
Structure type
Union type
Function type
Pointer type

---
Structure Types
A structure type describes a sequentially allocated nonempty set of member objects, each of which has an optionally specified name and possibly distinct type.

---
Union Types
A union type describes an overlapping nonempty set of member objects, each of which has an optionally specified name and possibly distinct type.

---
Pointer Types
A pointer type may be derived from a function type, an object type, or an incomplete type, called the referenced type. A pointer type describes an object whose value provides a reference to an entity of the referenced type. A pointer type derived from the referenced type T is sometimes called ‘‘pointer to T’’.

---
Types
Arithmetic types and pointer types are collectively called scalar types. Array and structure types are collectively called aggregate types.
Alignment requirement that objects of a particular type be located on storage boundaries with addresses that are particular multiples of a byte address

---
Storage Class
At most, one storage-class specifier may be given in the declaration specifiers in a declaration.
A declaration of an identifier for an object with storage-class specifier register suggests that access to the object be as fast as possible.
The implementation may treat any register declaration simply as an auto declaration. However, whether or not addressable storage is actually used, the address of any part of an object declared with storage-class specifier register cannot be computed, either explicitly (by use of the unary & operator ) or implicitly (by converting an array name to a pointer). Thus, the only operator that can be applied to an array declared with storage-class specifier register is sizeof.

---
Storage Class
At most, one storage-class specifier may be given in the declaration specifiers in a declaration.
A declaration of an identifier for an object with storage-class specifier register suggests that access to the object be as fast as possible.
The implementation may treat any register declaration simply as an auto declaration. However, whether or not addressable storage is actually used, the address of any part of an object declared with storage-class specifier register cannot be computed, either explicitly (by use of the unary & operator ) or implicitly (by converting an array name to a pointer). Thus, the only operator that can be applied to an array declared with storage-class specifier register is sizeof.