Bit Operations
A bitwise operators operates on one or more bit patterns at the level of their individual bits.

---
Bitwise right shift operator
 Syntax
shift-expression >> additive-expression
Each of the operands shall have integer type.
The result of E1 >> E2 is E1 right-shifted E2 bit positions.
If E1 has an unsigned type or if E1 has a signed type and a nonnegative value, the value of the result is the integral part of the quotient of E1 / (2 power E2).
if positive value Zeros are padded for moved bits and if negative whether 1 or 0 is padded is implementation dependent

---
Bitwise left shift operator
shift-expression << additive-expression
Each of the operands shall have integer type.
The result of E1 << E2 is E1 left-shifted E2 bit positions;
Vacated bits are filled with zeros.
If E1 has an unsigned type, the value of the result is E1 x 2 powerE 2. If E1 has a signed type and nonnegative value, and E1 x 2 power E2.
Zeros are padded for moved bits
If E1 is an negative value whether 0 is padded or 1 is padded for moved bits is implementation specific

---
Bitwise AND operator
AND-expression & equality-expression
Bitwise “ & “ works like logical “ && “ except that logical ” && “ works on bytes(int,char,float,...) where as bitwise “ & “ works on each bit on given operands
The result of the binary “ & “ operator is the bitwise AND of the operands (that is, each bit in the result is set if and only if each of the corresponding bits in the given operands is set).

---
Bitwise OR operator
AND-expression | equality-expression
Bitwise “ | “ works like logical “ || “ except that logical ” || “ works on bytes(int,char,float,...) where as bitwise “ | “ works on each bit on given operands
The result of the binary “ | “ operator is the bitwise OR of the operands (that is, each bit in the result is set if any bit of the corresponding bits in the given operands is set).

---
Bitwise complement operator
~ complement-expression
The bitwise complement operator flips every bit. if you have a 1, it's a 0, and if you have a 0, it's a 1.

---
Exclusive OR
~complement-expression
The exclusive-or operation takes two inputs and returns a 1 if either one or the other of the inputs is a 1, but not if both are. That is, if both inputs are 1 or both inputs are 0, it returns 0.